## Slide 1: Packetmaster EX2 WEB GUI Training
High Performance
Desktop Network Packet Broker
V 2.1.1.0

## Slide 2: Content
This training is intended to enable users of the Cubro Packetmaster EX2 to deploy and manage it via the Web GUI.
The Web GUI is designed to work with all standard web browsers such as:
  Microsoft Internet Explorer
  Mozilla Firefox
  Google Chrome
  …

## Slide 3: First Start
Connect to the EX2 via web browser
Download latest software version and upgrade the EX2
Change IP address configuration according to your requirements
Define Users
Define Port Settings
Define Functionality (Filter rules,…)

## Slide 4: Default Configuration – EX2
Management Interface
  IP: 192.168.0.200
  Mask: 255.255.255.0
  GW: 192.168.0.1
Port Setup
  Port 1 to 4: Autoneg ON
  Port 5 to 6: 1G
Default Flows/Filters
  None
Web Login
  At 1st login user/password is NOT required.
  A superuser is defined by default but not active
    User: admin
    Password: cubro
      This user is a superuser with full rights.
ssh Login
  User: root
  Password: fucik1

## Slide 5: EX2 Ports
SFP/SFP+ Ports for 1G/10G also 10G Base-T SFP supported
Ethernet Management I/F for web GUI or SSH connection; Default IP is 192.168.0.200/24
In the Web GUI under "Ports" - "Port Status" every defined Port as well as its port number is viewable.
Base-T ports for 10M/100M/1000M

## Slide 6: Connection to EX2
Connect to your Cubro Packetmaster EX2 via the Management Interface
Ethernet Management
Enter the IP of the Packetmaster in your web browser (Factory default: 192.168.0.200)
Web Browser will not require a login with username and password after upgrade – more later

## Slide 7: Web GUI Start-Up Screen Rule Table
After login the Web GUI shows the active rules – "Rule Table"
The EX2 is usually delivered without any defined rules. Therefore the rule table will be empty.

## Slide 8: General Settings

## Slide 9: Device – General Parameters
Allows setting IP parameters of the management port, Upgrade the unit, Define Users for Web access,…

## Slide 10: Device User Management - Overview
By default the EX2 is delivered with a superuser with the following credentials:
  Username: admin
  Password: cubro
    This user is not active until checkbox is selected
Save – whenever a new user is added or anything is changed the "Save" button must be clicked
Login by username/password enabled/disabled. By default this is not active. When active logging in requires a username and password
Add additional users – can only be done by a superuser

## Slide 11: Device User Management – Add User
Only a superuser can add/delete users
3 different levels of user can be created
  Superuser – with all rights
  Write – can change rules and templates. Can not create users, change port settings, IP config or upgrade the SW of the unit.
  Read – read only
Save – whenever a new user is added or anything is changed the "Save" button must be clicked

## Slide 12: Device User Management – Add User
Username
Freeform description for easier identifcation of the user
User level – Superuser, Write and View
Password – min. 4 characters

## Slide 13: Device User Management – Delete/Change User
Only a superuser can delete users
One superuser must remain active and therefore the last superuser can not be deleted.
Delete User
Change User

## Slide 14: Device - IP Configuration
Configure Management Interface
  Set configuration for management interface
  When settings are changed the browser automatically connects to the new IP address

## Slide 15: IP Setup – Rescue via Serial Interface
If the IP Address of the EX2 is unknown connect via Serial Console to the unit
  Serial Parameters
  CLI Commands

## Slide 16: Device – Other Settings
ID Tag that is displayed in the Web GUI
Set Layer2 and MPLS transparency – see chapter Transparency
Set “Standard Mode” with up to 2000 rules or “IPv6 Mode” with up 500 rules
Set load-balancing mechanism (calculation method) – see Chapter Load-Balancing
When "Permanence" is checked rules are immediately saved into the Quicksave Save-Point once they are defined.

## Slide 17: Permanence
If selected - rules and port groups are immediately saved in the Quicksave Save-Point when the "Apply Rule" button is clicked in the "+Add Rule" menu

## Slide 18: Transparency
The EX2 is a Network Packet Broker (NPB) and is able to analyze packets for filtering purposes; it is not a transparent
device such as a tap.
Some protocols such as Layer 2 Control Protocols (L2CP) and MPLS encapsulated packets might not pass through the EX2.
From Software Version 1.3.5.0 onwards the Web GUI of the EX2 offers a possibility to change the transparency mode.

## Slide 19: LACP/Link-OAM/ESMC Transparency
Protocol | EX2 Transparency | 
STP | Yes | Yes
LACP | No | Yes
Link OAM | No | Yes
ESMC | No | Yes
PTP | Yes | Yes
LLDP | Yes | Yes
VDP | Yes | Yes
PE-CSP | Yes | Yes
PNAC 802.1x | Yes | Yes
SPB | Yes | Yes
MMRP | Yes | Yes
MVRP | Yes | Yes
MSRP | Yes | Yes
MIRP | Yes | Yes
PAgP | Yes | Yes
CDP | Yes | Yes
UDLD | Yes | Yes
VTP | Yes | Yes
DTP | Yes | Yes
ISL | Yes | Yes
PVST | Yes | Yes
RSTP | Yes | Yes
MSTP | Yes | Yes
GMRP | Yes | Yes
GVRP | Yes | Yes
STP_ULFAST | Yes | Yes
VLAN_BRDGSTP | Yes | Yes
Full transparency of L2 control protocols

## Slide 20: MPLS Transparency
When the box is checked MPLS encapsulated packets are able to pass through the EX2. When not selected MPLS packets will be dropped.
MPLS tagged packets pass transparently through the EX2
MPLS tagged packets are dropped and do not pass through the EX2

## Slide 21: Device - Device Info
Scroll down for more information
Direct link to the latest firmware version for download or visit the URL directly http://www.cubro.net/cubro/update/ex2/

## Slide 22: Device - Device Info
Clicking displays Transceiver Details
Vendor
Product number
Wavelength
max. Link length
Thresholds
Alarms
Temperature
Voltage
Current
Optical Power Tx
Optical Power Rx

## Slide 23: Device - Firmware Upgrades
Software is available from http://www.cubro.net/cubro/update/ex2/
Release Notes are available from http://www.cubro.net/cubro/update/CHANGELOG.txt
Select firmware file to be uploaded
Install uploaded firmware file

## Slide 24: Port Settings

## Slide 25: Port Configuration
Specify port settings
Select port to configure (1-n)
Activate/Deactivate port
Select speed and duplex
Reboot is required when Port 5 and/or Port 6 is changed from 1G to 10G or 10G to 1G

## Slide 26: EX2 Port Speed and Duplex
Ports 1 to 4 (RJ45 Ports)

## Slide 27: EX2 Port Speed and Duplex
Ports 5 and 6 (SFP Ports)
  Speed 1G or 10G – change requires a reboot!

## Slide 28: EX2 Port Speed and Duplex
Ports 5 and 6 (SFP Ports)
  Speed and Duplex
Autoneg ON mode: Receiving link is established only if the Autoneg from the link partner is received.
Autoneg OFF mode must be used behind optical splitters; the link is established even without receiving Autoneg.

## Slide 29: Port Statistics
Port Statistics can be viewed and reset.
Summed result

## Slide 30: Port Status
Displays current status for all ports.
When Port is activated the Port Status is "PORT_UP"

## Slide 31: Functionality (Filtering, …)

## Slide 32: Filter Rules - Outline
Rules are applied in order of the priority.
  Priority is set for every rule; range between 0 (lowest) and 65535 (highest).
  Default priority is 32768.
Once a packet satisfies a matching filter the corresponding action is performed; the packet is no longer available for filtering.
  If two filters would match only the higher priority is applied!
If a packet does not satisfy a matching filter the packet is dropped.
Filter/Match
Priority
Action

## Slide 33: Entering Rules 1 – General Parameters
Click the "Add Rule" tab to enter new rules.
User-defined name of the rule
Detailed description of the rule
Rule Priority – to stack rules; Default Priority is 32768
Defines the Filter criteria
Defines the Action i.e. what should happen to the matched traffic

## Slide 34: Rule - Priority
The Cubro Packetmaster does not allow handling of an incoming packet twice. Once the packet matches a rule the packet is processed and there is no second opportunity to process this packet.
The priority field is a way to stack rules. The priority value can be anything between 0 and 65535. A higher value will match before a lower one.

## Slide 35: Stacking of Rules / Overlapping Flows
Required Functionality
Port 1: input
Port 2: input
Port 5: output – aggregate VLAN ID 100 traffic from Port 1 to 4
Port 6: output – aggregate all traffic from port 1 to 4
Rules/Flows:
Only VLAN ID100
All traffic incl. VLAN ID100
Filter/Match
Priority
Action
input=1,VLAN=100
40000
Output=5&6
input=2,VLAN=100
40000
Output=5&6
input=1
30000
Output=6
input=2
30000
Output=6

## Slide 36: Stacking of Rules / Overlapping Flows
Required Functionality
Port 1: input
Port 2: input
Port 5: output – aggregate VLAN ID 100 traffic from Port 1 to 4
Port 6: output – aggregate all traffic from port 1 to 4
Only VLAN ID100
All traffic incl. VLAN ID100

## Slide 37: Traffic inside Packetmaster
First matching filter processes the packet
CRC check
Priority 65535
Priority 65534
Priority 65533
Priority 65532
Filter 5
Priority 65531
Filter 6
Priority 65530
Filter
Priority 00001
Filter n
Priority 00000
No match
Action 1
Action n
Action 3
Filter 1
Filter 2
Filter 3
Filter 4

## Slide 38: Overlapping Filters
All traffic
http traffic only
Only one IP inside http
Sometimes the same traffic is desired at multiple outputs.
Output 1
Output 1,2,3
Output 1,2
  Assign highest priority to smallest traffic portion (most detailed filter criteria)
  Send traffic to all other ports where needed
  Continue with setup for other filters
input=6,IP, TCP Port 80
60000
Output=1,2,3
input=6,TCP Port 80
50000
Output=1,2
input=6
40000
Output=1

## Slide 39: Overlapping Filters
input=6,IP, TCP Port 80
60000
Output=1,2,3
input=6,TCP Port 80
50000
Output=1,2
input=6
40000
Output=1

## Slide 40: Entering Rules 2 – Match Fields
IP masks are entered in CIDR notation – e.g. /24
If VLAN filtering is required chose “match tagged traffic only”
Select ports to apply rules
Separator e.g. 1,3 or ranges e.g. 2-4
If empty the rule is valid for any incoming traffic  valid for all inputs

## Slide 41: Match Fields – important
Empty fields are like a wildcard and not considered further  to be considered as any value
To filter out a full duplex communication requires two filter rules.
input=1
32768
Output=2,3
input=2
32768
Output=1,3
Aggregated output

## Slide 42: Match Fields - Examples
Filter out full communication of IP 10.0.0.1 to 10.0.0.2  2 Filters required
Use the Swap Button to exchange Source and Destination

## Slide 43: Entering Rules 3 - Actions
Selects output ports for matching packets
Separator e.g. 1,3 or ranges e.g. 2-4. Note that each defined Port carries the same traffic.
Removes matched packets
Sends packets to a group of ports – required for Load-Balancing (see later)
Additional actions to output action – modifies the packet; e.g. adds a VLAN tag

## Slide 44
Problem: How to identify on an aggregated output at which port the traffic originally arrived?
Solution: Use VLAN Push function. Add a specific VLAN tag on each input port.
input=1
32768
Output=6 + VLAN ID 101
input=2
32768
Output=6 + VLAN ID 102
Aggregated output incl. VLAN IDs for identification
input=3
32768
Output=6 + VLAN ID 103
Match+Actions - Example

## Slide 45: VLAN push
input=1
32768
Output=6 + VLAN ID 101
input=2
32768
Output=6 + VLAN ID 102
input=3
32768
Output=6 + VLAN ID 103

## Slide 46: Rule Table 1
Click "Rule Table" to display all active rules.
Shows total number of flows/rules used
Summed result

## Slide 47: Rule Table 2
Editing/Copying/Deleting Rules
Edit rule (only Output Actions can be edited)
Create new rule using the current one as basis
Delete this rule
Hides/Unhides columns
e.g.
Saves rules to the Quicksave memory – see chapter “Save-Points”
Note: If rules are not saved and the unit is rebooted the rules are deleted.
Deletes all active rules.
Stored rules are not deleted!
Resets all counters in "Rule Table"

## Slide 48: Packetmaster EX IPv6 Filtering

## Slide 49: IPv6 Filtering - Overview
In the default configuration the Packetmaster EX allows IPv4 Filtering only.
In the default configuration IPv6 Packets can be
  Aggregated
  Filtered for Layer 2 parameters (MAC and VLAN). IPv6 Address and/or UDP/TCP Port Numbers; filtering is not possible.
To filter on IPv6, the Database (DB) mode needs to be changed. Afterwards IPv6 filtering is possible.

## Slide 50: Change DB Mode to IPv6
Go to Device – Other Settings – DB Mode and select “Support for granular IPv6 matching” and press “Save” then “Reboot”.
After the reboot the unit is able to handle IPv4 and IPv6 traffic and filtering as well.

## Slide 51: IPv6 Address Filtering
Select Add Rule and change Match Fields
needs to be set to Custom
needs to be set to 0x86dd which means IPv6
needs to be set to
ipv6_src = Source Address
ipv6_dst=Destination Address

## Slide 52: Example: Source & Destination Filter
Source: 5555:11:c0a8:a::8551
Destination: 5555:11:c0a8:a::8552
Extra Custom Match:
  ipv6_src=5555:11:c0a8:a::8551,ipv6_dst=5555:11:c0a8:a::8552

## Slide 53: Rule Table View
Rule Table shows the IPv6 filter correctly

## Slide 54: TCP/UDP Filtering on IPv6 traffic
Extra Custom Match
  udp6 for UDP or use Protocol Number 17
  tcp6 for TCP or use Protocol Number 6
  tp_src=<Source Port Nr.> or use
    udp_src=<UDP Source Port Nr.>
    tcp_src=<TCP Source Port Nr.>
  tp_dst=<Destination Port Nr.> or use
    udp_dst=<UDP Destination Port Nr.>
    tcp_dst=<TCP Destination Port Nr.>

## Slide 55: Example: UDP Source Port Filter
UDP Source Port: 1000
Extra Custom Match:
  udp6,tp_src=10000

## Slide 56: Example: Address and Port Filter

## Slide 57: IPv6 Summary
Protocol set to Custom
EtherType set to 0x86dd
Extra Custom Match
  IPv6 Destination: ipv6_dst=<ipv6/netmask>
  IPv6 Source Address: ipv6_src=<ipv6/netmask>
  UDP: udp6
  TCP: tcp6
  Source Port: tp_src=<Port Number>
  Destination Port: tp_dst=<Port Number>

## Slide 58: Packetmaster EX TCP Flag Filtering

## Slide 59: TCP Flag Filtering
Packetmaster EX allows the user to filter on TCP Flags such as SYN, ACK, RST, etc.
To use this capability via the Web GUI of the EX we have a special field called Extra Custom Match that is located in the Add Rule menu.

## Slide 60: TCP Flag possibilities
EX supports a bitwise match on the TCP flags including a mask. The flags and mask are 16-bit numbers written in decimal or in hexadecimal prefixed by 0x. Each1-bit in mask requires that the corresponding bit in flags must match. Each 0-bit in mask causes the corresponding bit to be ignored.
Alternatively, the flags can be specified by their symbolic names, each preceded by either + for a flag that must be set, or - for a flag that must not be set, without any other delimiters between the flags. Flags not mentioned are considered wildcards. For example, tcp_flags=+syn-ack matches TCP SYNs that are not also ACKs.

## Slide 61: Symbolic Names
TCP protocol currently defines 9 flag bits, and additional 3 bits are reserved (must be transmitted as zero), see RFCs 793,3168, and 3540. The flag bits are, numbering from the least significant bit:
Bit | Symbolic Name | Description
0 | fin | No more data from sender
1 | syn | Synchronize Sequence Numbers
2 | rst | Reset the connection
3 | psh | Push function
4 | ack | Acknowledgement field significant
5 | urg | Urgent pointer field significant
6 | ece | ECN Echo
7 | cwr | Congestion Windows Reduced
8 | ns | Nonce Sum
9-11 | - | Reserved
12-15 | - | Must be zero

## Slide 62: Use of Extra Custom Match
needs to be set to IP/TCP
needs to be set to tcp_flags=<symbolic name>
+syn-ack means that it filters out all syn messages that are not acknowledged.

## Slide 63: Rule Table View
Rule Table shows the filter correctly.

## Slide 64: Group Settings (Load-Balancing)

## Slide 65: +Add Group and Group Table
"+Add Group" – allows the user to define a group of ports e.g. for load-balancing applications.
Group Table – shows the defined groups

## Slide 66: +Add Group
Select a Group ID. Important because a rule needs to be defined that uses this ID as an action.
Defines the type of group. For load-balancing "Select" has to be used.

## Slide 67: Load-Balancing via Select Group
e.g. Ports 1 through 4 should load-balance the traffic that is received by Port 6
Steps
  Define Group ID=1 as Type=Select with P1 to P4
  Define Load-Balancing Hash-Key
  Verify Group Settings via Group Table
  Define rule from P6 to Group ID1

## Slide 68: Group Definition
Important: for load-balancing the type needs to be "Select".
Traffic is only forwarded to the relevant output port if the watch port status is "Link-Up". Usually the “Output to Ports” and "Watch Port" are set to the same value. If the "Watch-Port" status is "Link-Down" the traffic is forwarded to another port within the group.
Green color shows that the bucket is correctly defined.
Set the output port of each bucket = set the ports that belong to this group.

## Slide 69: Group Definition
A group can include up to 16 ports (buckets 0 through 15).
Traffic is distributed within the ports of the group.
Distribution is based on a calculated hash-key.
Hash-key calculation criteria is user selectable

## Slide 70: Group Table
Verify the group settings
Change hash-key
Opens Hash-key settings.
Select means that a packet is handled only by a single action. Either sent to P1 or P2 or P3 or ‘’P4

## Slide 71: Hash-Key
Hash-Key settings are found in "Device" – "Other Settings" – "Group Hash Algorithms"
opens up
Selectable Hash-key criteria

## Slide 72: Session-aware Load-balancing
Session-aware = every packet that belongs to the same conversation is sent to the same physical output port within the group.
Conversation association is done by examining selected fields within each packet and performing a mathematical algorithm called hash key calculation to consistently separate and distribute traffic to specific ports within a load balanced group.
Packets that result in the same Hash-key value are always sent to the same physical output port.

## Slide 73: Hash-key example for IP Source Address

## Slide 74: Hash-key for two or more criteria
Hash value is calculated over both fields
As a result the hash-key is the same for both directions  Layer 3 session aware !

## Slide 75: Define Rule to forward traffic to Group

## Slide 76: Additional Group Actions
In addition to straight output of a packet it is also possible to modify the packets.

## Slide 77: Filtering and Load-balancing
Filtering and load-balancing is possible at the same time.
Filtering is done at the inputs and only filtered packets will be further processed.
Only packets arriving at P1 with IP Source 10.0.0.1 will be sent to group 1

## Slide 78: Other Group Types
ALL actions will be executed simultaneously. Traffic arriving will be sent out at P1 AND P2 and at the same time the IP Destination will be changed to 20.0.0.1 for P1 and to 20.0.0.2 for P2.
FF = Fast Failover; Traffic is sent to P1. If P1 goes down the traffic is sent to P2.

## Slide 79: Save Setups

## Slide 80: Save-Points
Save-Points allow the user to save rules and port settings.
Exports the selected Save-Point for backup purposes
Download a Save-Point to the EX2
Select which Save-Point is loaded after a reboot
Saves Port Configuration
Saves Rule Configuration
Rules that are saved via “Make Rules and Groups permanent” in the Rule Table menu

## Slide 81: Applications (Apps)

## Slide 82: Apps - Applications
Apps are special pieces of software that run inside the EX2 and in parallel to the standard Packetmaster Software.
Configures the App

## Slide 83: Heartbeat App

## Slide 84: SNMP App
Runs a SNMP server and sends SNMP traps to a SNMP receiver

## Slide 85: ARP Responder App
Responds to ARP requests. Used in GRE encapsulation/decapsulation applications.

## Slide 86: Reset SFP App
IP Adress:
  IP: 192.168.2.250
  Maske: 255.255.255.0
  Gateway : 192.168.2.1
Default Flows/Filter:
  P1 <-> P2; aggr. auf P3
  P5 <-> P6; aggr. auf P4
Port Setup:
  P1 bis 4: Autoneg ON
  P5 und 6: 1G

## Slide 87: Heartbeat Bypass App
EX2 controls a Cubro Bypass Switch

## Slide 88: Heartbeat Bypass App

## Slide 89: Functions not available in the Web GUI
Please note that not all functions of the EX2 are implemented in the Web GUI.
Full functionality like GRE encapsulation/decapsulation or sFlow generation of the EX2 is available via SSH CLI access.
Contact us if you need more details.

## Slide 90: Cubro Support Portal
Register at the Cubro Support Portal – http://support.cubro.com
Get access to our technical support engineers

## Slide 91: Contact Information
If you have any additional question or need help contact us.
Cubro Acronet GesmbH
Geiselbergstr. 17/6.OG
1110 Vienna
Austria
Tel.: +43 1 29826660
Fax: +43 1 2982666399
Email: support@cubro.net
www.cubro.net